## Slide 1: MSG-1 – The Challenges!
David Taylor
SatSignal Software
Edinburgh

## Slide 2: Today’s Talk
What is MSG-1?
What do I need to receive MSG-1?
What happens to WEFAX/PDUS?
What is LRIT/HRIT?
What are the hardware implications?
What about MSG-2?

## Slide 3: What is MSG-1?
New satellite covering Europe and Africa
Replaces Meteosat-7
Higher resolution – more pixels
More atmospheric detail – more channels
Faster scanning – better movement display
Currently in commissioning trials phase

## Slide 4: Transmission Differences
Requirements
  Much more information to transmit
  Higher accuracy required
Solution
  Use digital not analogue
  Meet full professional needs with HRIT
  Meet less demanding needs with LRIT
  Use both lossy and lossless compression

## Slide 5: What are HRIT and LRIT?
High Rate Image Transmission – 1-2 Mb/s
Low Rate Image Transmission – 128Kb/s
Data
  in packets
  not a continuous stream
Channels
  transmitted simultaneously
  not separately

## Slide 6: OSI Seven Layer Model
Splits processing into functions
Well defined interface between layers
Examples going down the layers…
  Getting the image the right way up!
  Assembling image segments
  Decompressing, e.g. JPEG
  Decryption
  Error correction
  Demodulation

## Slide 7: Data Views – Top-down
How is an image built up?
In horizontal strips
May need many strips per image
One strip lost doesn’t loose whole image
An image strip is a single computer file
Files are split into packets for transmission

## Slide 8: Data Views – Bottom Up
BPSK signal from satellite
Demodulated digital data
Viterbi decoding
Reed-Solomon decoding
Packets to transport layer
Assembled into files

## Slide 9: New Processing Challenges
Data rate is 2GB/hour – what to do with it?
Data is 8-, 10- and 12-bit precision
  How are you going to display this?
JPEG is 8-bit and 12-bit
  Do you have 12-bit JPEG software?
Compression is JPEG and Wavelet Transform
  Do you have wavelet transform software?
GOES may use a different compression
  Do you have working RICE-transform software?

## Slide 10: Receiving Meteosat-8
One power-amplifier broken (of four)
Alternative dissemination via DVB service
Same as Digital TV from satellites
Packets are data rather than images
Broadcast – if you miss a file, it’s lost!
Needs a dish, LNB and a card in your PC
Can learn by receiving ATOVS data today

## Slide 11: The Gremlin in MSG-1?

## Slide 12: DVB Reception Hardware
DVB – Digital Video Broadcasting
Dish – 88cm typical
11GHz – so needs accurate pointing!
LNB – RF amplifier, LO and mixer
Cable carries 1GHz range IF
Card in PC
  demodulates IF to packets
  controls LNB oscillator band etc.

## Slide 13: DVB – Typical Installation

## Slide 14: DVB – Low-Noise Block

## Slide 15: DVB Reception - Software
Drivers
  supplied with card
Data decoding software
  T-Systems (Tellique)
  Reads username/password from file you edit
  USB dongle for “encrypted” data
File decoding software
  ATOVS Reader
  MSG Reader

## Slide 16: DVB – Software setup 1

## Slide 17: DVB – Software setup 2

## Slide 18: DVB – Software setup 3

## Slide 19: PC Requirements
NOT your main PC
PC to be dedicated to data capture
Networked to processing PC
5 volt PCI slot for SkyStar 2 card
ATOVS – 700MHz CPU / 512MB RAM
MSG-1 – 2 GHz P4 / 1GB RAM / disk!
Can you bend the rules?

## Slide 20: Challenges
All the data – 2GB/hour uncompressed
No provision for data subset on DVB
What do you want to keep?
  Which channels?
  Region subset?
Full resolution visible image is 62MPixels, that’s 186MB in 24-bit colour!

## Slide 21: MSG-2 in the future
Compatibility at the file level
Different hardware for direct reception

## Slide 22: MSG Data Manager – Screenshot

## Slide 23: MSG Data Manager – Performance
1GHz PC ( 2GHz recommended)
512MB RAM (1GB recommended)
Processing time for all 12 MSG-1 channels
  2 minutes to read and decompress data
  15 seconds to save images
Source was 814 files, 64.4MB
Destination was 12 image files, 35.1MB
  PNG or JPEG compressed

## Slide 24: Conclusions
MSG-1 trials are here now!
New hardware and software required
Have learned with ATOVS
Not complex – but novel
Massive amounts of data
Need to learn how to manage this!

## Slide 25: Acknowledgments
To Eumetsat
  For making sample data and decoding software available
To you all
  For your support over the years
To individuals in RIG
  For doing so much for the hobby
  Negotiating with Eumetsat and RF agencies
  Making low-cost hardware available

## Slide 26: Your Questions?